Cs460
Part 1.
Questions in mk file:
1. The first statement takes the ts.s file and uses the GNU assembler to compile it so the linker can understand the code for ARM.

2. The second statement uses the GCC compiler to compile the t.c file into it’s .o form for the linker as well.

3. The third statement is the last step in compiling the source code, using the -ld GNU linker to combine all the object files and read instructions from the t.ld file. The t.elf file contains extra information.

4. Since we are going to be loading data to a specific memory address it is better to work with our program in the raw binary executable format. This line creates the binary executable for us. The contrary Executable Linkable Format which has symbol look-ups and relocatable table and other sections are unnecessary for our purposes.

Question in t.ld file: Part 1. Q1.2
Memory map of image file:
It’s just the locations of the variables and assembly data in memory.

QUIZ:
Question 1:

4 byte integer per pixel